## Slide 1: Universal Request ID (URI)
Bus Cluster
WW15’19

## Slide 2: Goal
Give an introduction of URI, but mainly show how use URI to debug with BUS trackers

## Slide 3: Introduction
URI is an identifier attached to “every” transaction that flows through ATOM
URI is standard used by the SOC and Intel IP
  Strong ASK from our customers
URI is synthesizable instrumentation RTL (emulation friendly)
The URI implementation is owned by RTL team and RTL team is responsible to maintain it

## Slide 4: Benefits and Use
URI simplifies debugging as you can track and easily identify transaction moving through GRT
  All trackers should be printing the URI
  This includes ATOM integration into our SOC’s
URI simplifies validation as it can use a key to lookup a transaction
  If URI does not work validation collateral will not work

## Slide 5: URI Files
URI is common INTEL collateral, currently we have a copy to ease our implementation in
    $MODEL_ROOT/subIP/uri_global
  Struct Defines
      uri_core_defs.vh
  Macro Defines
      uri_macros.sv
  Source Type Defines
      uri_src_type.sv, uri_types.e
      Example: uri_atom_l1_evic
      Currently we have the uri_atom prefix that subject to change to uri_
      The Suffix should be at most 7characters

## Slide 6: URI Contents
URI struct is composed of 3 sub structs:
  PID (Parent ID) – Parent ID
  LID (Local ID) – My ID
  TID (Transaction ID) – Initiator transaction ID
Each ID sub struct has:
package, source, instance, thread, counter
Transaction
counter
Thread ID for multi
Thread/cores
sources
Source Instance ID
e.g.
Module #2
Enumerated Source ID
(device+source)
Package ID for
multiple
package projects

## Slide 7: URI Spawning
A request can spawn a request that is reflected in the new URI
    For example we have a initial request from the MEC. This an RFO missing the L2 and victimizing a dirty line
PID | LID | TID
_____NA_000000 | ld_aloc_1000004 | ld_aloc_1000004
PID | LID | TID
ld_aloc_1000004 | l2_evic_1000000 | ld_aloc_1000004
Spawn

## Slide 8: Spawn in bus
L2 Evict
Prefetch
IDI Selfsnoop
PSMI Mirror?
…

## Slide 9: Tracker and Monitors
MEC_BUS_CA0.trk
BBL_L2_CA0.trk
BIU_BGF_CA0.trk
BUS_XQ_DOB_CA0.trk
L2Q_BBL_CA0.trk
L2Q_XQ_CA0.trk
SNPQ_CA0.trk
idi_mon_trk.out
Monitors
bus_bbl_l2_mon.svh
bus_bgf_piclet_mon.svh
bus_biu_bgf_mon.svh
bus_l2q_xq_mon.svh
bus_prefetcher_mon.svh
bus_snp_mon.svh
bus_xq_bbl2dob_mon.svh
csh_mec2bus_mon.svh

## Slide 10: Example
RFO missing the L2 (causing an L2 eviction), but hitting the other core in M-State
This will create 3 spawns
  L2 Evict
  SnpINV
  L2 Prefetch

## Slide 11: MEC Tracker
=========================================================================================================================================================================
Log File | Time | addr | URI PIDSrc_TrInCtr_LIDSrc_TrInCr_TIDSrc_TrInCr | RID | CoreId | ID | Ack | Phase | ExtType | Set
=========================================================================================================================================================================
0MEC_BUS | 4988957 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | 1 | MEC2BUS_REQ | DCU_READ | 000
0MEC_BUS | 4989746 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 9 | 3 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4989746 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 10 | 2 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4989746 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 11 | 1 | -- | -- | BUS2MEC_SNP_REQ | NA | 000
0MEC_BUS | 4989746 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 12 | 0 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4990804 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 9 | 3 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 4990804 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 10 | 2 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 4990804 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 12 | 0 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 4993697 | 000011000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | -- | 1 | -- | 1 | -- | DCU_BIU_PREF | 001
0MEC_BUS | 4994223 | 000011000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | -- | 1 | -- | 1 | -- | DCU_BIU_PREF | 002
0MEC_BUS | 4994486 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 13 | 3 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4994486 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 14 | 2 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4994486 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 15 | 1 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4994486 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 16 | 0 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4994749 | 0000110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | -- | 1 | -- | 1 | -- | DCU_BIU_PREF | 003
0MEC_BUS | 4995538 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 13 | 3 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 4995538 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 14 | 2 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 4995538 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 15 | 1 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 4995538 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 16 | 0 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 5010015 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 17 | 3 | -- | -- | BUS2MEC_SNP_REQ | PR2I | 000
0MEC_BUS | 5010015 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 18 | 2 | -- | -- | BUS2MEC_SNP_REQ | PR2I | 000
0MEC_BUS | 5010015 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 19 | 1 | -- | -- | BUS2MEC_SNP_REQ | PR2I | 000
0MEC_BUS | 5010015 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | -- | -- | BUS2MEC_SNP_REQ | PR2I | 000
0MEC_BUS | 5011067 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 17 | 3 | -- | -- | MEC2BUS_SNP_RSP | PR2I | 000
0MEC_BUS | 5011067 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 18 | 2 | -- | -- | MEC2BUS_SNP_RSP | PR2I | 000
0MEC_BUS | 5011067 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 19 | 1 | -- | -- | MEC2BUS_SNP_RSP | PR2I | 000
0MEC_BUS | 5011067 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | -- | -- | MEC2BUS_SNP_RSP | PR2I | 000
0MEC_BUS | 5011856 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | MEC2BUS_SNP_DATA | PR2I | 000
0MEC_BUS | 5014223 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | MEC2BUS_DATA | PR2I | 000
0MEC_BUS | 5014486 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | MEC2BUS_DATA | PR2I | 000
0MEC_BUS | 5014749 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | MEC2BUS_DATA | PR2I | 000
0MEC_BUS | 5015012 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | BUS2MEC_MEM_COMPL | PR2I | 000
0MEC_BUS | 5015012 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | MEC2BUS_DATA | PR2I | 000
0MEC_BUS | 5034223 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | -- | BUS2MEC_MEM_GO | DCU_READ | 000
0MEC_BUS | 5041067 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | -- | BUS2MEC_DATA | DCU_READ | 000
0MEC_BUS | 5041067 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | -- | BUS2MEC_DATA | DCU_READ | 000
0MEC_BUS | 5043697 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | -- | BUS2MEC_DATA | DCU_READ | 000
0MEC_BUS | 5044223 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | -- | BUS2MEC_MEM_COMPL | DCU_READ | 000

## Slide 12: IDI tracker
----------------+----------------+----------------+---------+---------------+--+--+----------------+------------+----------------------+-------------+-+---+-+-+--+-+-+-
| | | | | | | | | | | |A| | | | |S| |N
| | | | | | | | | | | |d| | | | |e|P|o
| | | | | | | | | | | |r| |C| | |l|r|n
| | | | | | | S| D | | | |P| |q| | L|f|i|T
| | | | | | | R| S | | | |a| |i| | e|S|o|e
| | | | | | | C| T | | | |r| C|d|L| n|n|r|m
| | | | | | D| | | | | |i| q|P|p| g|o|i|p
| | | | | | I| I| I | IDI | IDI | ADDRESS/ |t| i|a|i| t|o|t|r
| URI_PID | URI_LID | URI_TID | GUID | TIME | R| D| D | CHANNEL | PKT_TYPE |Total_Credits|y| d|r|d| h|p|y|o
|----------------+----------------+----------------+---------+---------------+--+--+----------------+------------+----------------------+-------------+-+---+-+-+--+-+-+-
_____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 00000006: 4997500 RX 0 0 C2U_REQUEST DRd_Opt 0000011000000 0 2 0 1 0 1 0 0
ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 00000008: 5000000 RX 0 0 C2U_REQUEST DRd_Opt_Pref 0000011000040 0 3 0 1 0 0 0 0
ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 0000000A: 5002500 RX 0 0 C2U_REQUEST DRd_Opt_Pref 0000011000080 0 0 0 1 0 0 0 0
ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 00000008: 5002500 TX 0 0 U2C_RESPONSE GO_F --------------- 3 0 0 --------
ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 00000006: 5002500 TX 0 0000000000000001 U2C_REQUEST BACK_INV 0000011000000 0 ----- 1 --------
ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 0000000A: 5005000 TX 0 0 U2C_RESPONSE GO_F --------------- 0 0 0 --------
ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 0000000C: 5007500 RX 0 0 C2U_REQUEST DRd_Opt_Pref 00000110000C0 0 1 0 1 0 0 0 0
ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 0000000E: 5010000 RX 0 0 C2U_REQUEST WbMtoI 0000000200000 0 40 0 1 0 0 0 0
ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 0000000C: 5010000 TX 0 0 U2C_RESPONSE GO_F --------------- 1 0 0 --------
ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 00000008: 5010000 TX 0 0 U2C_DATA -------------------------------------- 3 0 0 --------
ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 0000000E: 5012500 TX 0 0 U2C_RESPONSE GO_WRITE_PULL --------------- 40 0 0 --------
ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 00000008: 5012500 TX 0 0 U2C_DATA -------------------------------------- 3 0 0 --------
ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 0000000A: 5015000 TX 0 0 U2C_DATA -------------------------------------- 0 0 0 --------
ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 0000000A: 5017500 TX 0 0 U2C_DATA -------------------------------------- 0 0 0 --------
ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 0000000C: 5020000 TX 0 0 U2C_DATA -------------------------------------- 1 0 0 --------
ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 00000006: 5022500 RX 0 0 C2U_RESPONSE RSP_I_FWD_MO --------------------------------
ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 00000006: 5022500 RX 0 0 C2U_DATA BYTE_ENABLE_FFFF_BFFF --------------------------------
ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 0000000C: 5022500 TX 0 0 U2C_DATA -------------------------------------- 1 0 0 --------
ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 00000006: 5025000 RX 0 0 C2U_DATA BYTE_ENABLE_FFFF_FFFF --------------------------------
ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 0000000E: 5027500 RX 0 0 C2U_DATA BYTE_ENABLE_DFFF_FFFF --------------------------------
_____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 00000006: 5027500 TX 0 0 U2C_RESPONSE GO_M --------------- 2 0 0 --------
ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 0000000E: 5030000 RX 0 0 C2U_DATA BYTE_ENABLE_FFFF_FFFF --------------------------------
_____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 00000006: 5035000 TX 0 0 U2C_DATA -------------------------------------- 2 0 0 --------
_____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 00000006: 5037500 TX 0 0 U2C_DATA -------------------------------------- 2 0 0 --------

## Slide 13: grep -h ld_aloc_1000004 *.trk | sort -n --field-separator='|' --key=2 | cut -c-169
0SNPQ | 4988168 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 62 | 0 | 1 | MEC2BUS_REQ | DCU_READ | 000 |
0MEC_BUS | 4988957 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | 1 | MEC2BUS_REQ | DCU_READ | 000
0BBL_L2 | 4989220 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 4 | -- | BBL REQ | L2_UOP_RLU | DCU_READ | 0 | 00001100 |
0L2Q_BBL | 4989220 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 18 | DCU_READ | 2 | 62 | 1 | Q_DCU_PREFIX | 0 | 0 |
0SNPQ | 4989483 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | -- | -- | -- | BBL2L2Q_REQ | -- | 000 | INT_S
0SNPQ | 4989746 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | -- | 0 | 0 | BBL2MEC_REQ | -- | 000 | INT_S
0SNPQ | 4989746 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | -- | 0 | 1 | BBL2MEC_REQ | -- | 000 | INT_S
0SNPQ | 4989746 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | -- | 0 | 2 | BBL2MEC_REQ | -- | 000 | INT_S
0SNPQ | 4989746 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | -- | 0 | 3 | BBL2MEC_REQ | -- | 000 | INT_S
0MEC_BUS | 4989746 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 9 | 3 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4989746 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 10 | 2 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4989746 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 11 | 1 | -- | -- | BUS2MEC_SNP_REQ | NA | 000
0MEC_BUS | 4989746 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 12 | 0 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0SNPQ | 4990278 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | -- | -- | -- | L2Q2SNPQ_RSP | -- | 000 | INT_S
0BBL_L2 | 4990541 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 4 | 0 | L2 RSP | L2_UOP_RLU | DCU_READ | 0 | 00001100 |
0SNPQ | 4990804 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | -- | 0 | 0 | MEC2BBL_RSP | -- | 000 | INT_S
0SNPQ | 4990804 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | -- | 0 | 2 | MEC2BBL_RSP | -- | 000 | INT_S
0SNPQ | 4990804 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | -- | 0 | 3 | MEC2BBL_RSP | -- | 000 | INT_S
0MEC_BUS | 4990804 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 9 | 3 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 4990804 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 10 | 2 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 4990804 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 12 | 0 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0BBL_L2 | 4991067 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 4 | -- | BBL LRU | L2_UOP_RLU | DCU_READ | 0 | 00001100 |
0XQ_DOB | 4991067 | -- | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | -- | 0 | L2_EVICTION | 1 | 00 | BBLal
0XQ_DOB | 4991067 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 000 | 1 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt | 1 | 3e | BBLa
0L2Q_BBL | 4991067 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 18 | BBL2L2Q_RSP | 2 | 62 | -- | Q_DCU_PREFIX | 0 | -- |
0XQ_DOB | 4991330 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 000 | 1 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt | 1 | 3e | GP R
0BBL_L2 | 4991593 | -- | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 5 | -- | BBL REQ | L2_UOP_EVICT | -- | 0 | -- |
0BBL_L2 | 4992908 | 000000200000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 5 | 0 | L2 RSP | L2_UOP_EVICT | -- | 0 | 00000020 |
0XQ_DOB | 4993434 | 200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 000 | 0 | L2_EVICTION | 1 | 00 | DO
0MEC_BUS | 4993697 | 000011000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | -- | 1 | -- | 1 | -- | DCU_BIU_PREF | 001
0BBL_L2 | 4993960 | -- | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 5 | -- | L2 DATA | L2_UOP_EVICT | ACTUAL DATA | -- | -- |
0BBL_L2 | 4993960 | -- | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 5 | -- | L2 DATA | L2_UOP_EVICT | ACTUAL DATA | -- | -- |
0BBL_L2 | 4993960 | 000000200000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 5 | -- | L2 DATA | L2_UOP_EVICT | -- | 0 | -- |
0BBL_L2 | 4993960 | 000000200000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 5 | -- | L2 DATA | L2_UOP_EVICT | -- | 0 | -- |
0SNPQ | 4994223 | 200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | -- | -- | -- | BBL2L2Q_REQ | -- | 000 | BI_S
0BBL_L2 | 4994223 | 000011000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 6 | -- | BBL REQ | L2_UOP_RLUP | DCU_BIU_PREF | 0 | 00001100 |

## Slide 14: grep -h ld_aloc_1000004 *.trk | sort -n --field-separator='|' --key=2 | cut -c-169
0BBL_L2 | 4994223 | 000011000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 6 | -- | BBL REQ | L2_UOP_RLUP | DCU_BIU_PREF | 0 | 00001100 |
0XQ_DOB | 4994223 | 0 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 000 | 0 | -- | 0 | 00 | DOB Dat
0XQ_DOB | 4994223 | 0 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 000 | 0 | -- | 0 | 00 | DOB Dat
0L2Q_BBL | 4994223 | 000011000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 19 | DCU_BIU_PREF | 2 | 0 | 1 | Q_PREF_PREFIX | 10 | 0 |
0MEC_BUS | 4994223 | 000011000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | -- | 1 | -- | 1 | -- | DCU_BIU_PREF | 002
0SNPQ | 4994486 | 200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | -- | 0 | 0 | BBL2MEC_REQ | -- | 000 | BI_S
0SNPQ | 4994486 | 200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | -- | 0 | 1 | BBL2MEC_REQ | -- | 000 | BI_S
0SNPQ | 4994486 | 200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | -- | 0 | 2 | BBL2MEC_REQ | -- | 000 | BI_S
0SNPQ | 4994486 | 200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | -- | 0 | 3 | BBL2MEC_REQ | -- | 000 | BI_S
0MEC_BUS | 4994486 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 13 | 3 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4994486 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 14 | 2 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4994486 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 15 | 1 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0MEC_BUS | 4994486 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 16 | 0 | -- | -- | BUS2MEC_SNP_REQ | CMP2S | 000
0BBL_L2 | 4994749 | 000011000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 7 | -- | BBL REQ | L2_UOP_RLUP | DCU_BIU_PREF | 0 | 00001100 |
0L2Q_BBL | 4994749 | 000011000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 20 | DCU_BIU_PREF | 2 | 0 | 1 | Q_PREF_PREFIX | 0 | 0 |
0MEC_BUS | 4994749 | 0000110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | -- | 1 | -- | 1 | -- | DCU_BIU_PREF | 003
0SNPQ | 4995012 | 200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | -- | -- | -- | L2Q2SNPQ_RSP | -- | 000 | BI_S
0BBL_L2 | 4995275 | 0000110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 8 | -- | BBL REQ | L2_UOP_RLUP | DCU_BIU_PREF | 0 | 00001100 |
0L2Q_BBL | 4995275 | 0000110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 21 | DCU_BIU_PREF | 2 | 0 | 1 | Q_PREF_PREFIX | 11 | 0 |
0SNPQ | 4995538 | 200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | -- | 0 | 0 | MEC2BBL_RSP | -- | 000 | BI_S
0SNPQ | 4995538 | 200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | -- | 0 | 1 | MEC2BBL_RSP | -- | 000 | BI_S
0SNPQ | 4995538 | 200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | -- | 0 | 2 | MEC2BBL_RSP | -- | 000 | BI_S
0SNPQ | 4995538 | 200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | -- | 0 | 3 | MEC2BBL_RSP | -- | 000 | BI_S
0BBL_L2 | 4995538 | 000011000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 6 | 0 | L2 RSP | L2_UOP_RLUP | DCU_BIU_PREF | 0 | 00001100 |
0MEC_BUS | 4995538 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 13 | 3 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 4995538 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 14 | 2 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 4995538 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 15 | 1 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0MEC_BUS | 4995538 | 000000200000 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 16 | 0 | -- | -- | MEC2BUS_SNP_RSP | CMP2S | 000
0BBL_L2 | 4996064 | 000011000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 6 | -- | BBL LRU | L2_UOP_RLUP | DCU_BIU_PREF | 0 | 00001100 |
0BBL_L2 | 4996064 | 000011000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 7 | 0 | L2 RSP | L2_UOP_RLUP | DCU_BIU_PREF | 0 | 00001100 |
0XQ_DOB | 4996064 | 0 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 000 | 0 | -- | 0 | 00 | BI SN
0XQ_DOB | 4996064 | 11000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 001 | 2 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | BBLa
0L2Q_BBL | 4996064 | 000011000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 19 | BBL2L2Q_RSP | 2 | 0 | -- | Q_PREF_PREFIX | 10 | -- |
0XQ_DOB | 4996327 | 11000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 001 | 2 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | GP R
0BBL_L2 | 4996590 | 000011000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 7 | -- | BBL LRU | L2_UOP_RLUP | DCU_BIU_PREF | 0 | 00001100 |
0BBL_L2 | 4996590 | 0000110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 8 | 0 | L2 RSP | L2_UOP_RLUP | DCU_BIU_PREF | 0 | 00001100 |
0XQ_DOB | 4996590 | 11000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 002 | 3 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | BBLa

## Slide 15: grep -h ld_aloc_1000004 *.trk | sort -n --field-separator='|' --key=2 | cut -c-169
0XQ_DOB | 4996590 | 11000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 002 | 3 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | BBLa
0L2Q_BBL | 4996590 | 000011000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 20 | BBL2L2Q_RSP | 2 | 0 | -- | Q_PREF_PREFIX | 0 | -- |
0XQ_DOB | 4996853 | 11000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 002 | 3 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | GP R
0BBL_L2 | 4997116 | 0000110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 8 | -- | BBL LRU | L2_UOP_RLUP | DCU_BIU_PREF | 0 | 00001100 |
0XQ_DOB | 4997116 | 110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 003 | 4 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | BBLa
0L2Q_BBL | 4997116 | 0000110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 21 | BBL2L2Q_RSP | 2 | 0 | -- | Q_PREF_PREFIX | 11 | -- |
0XQ_DOB | 4997379 | 110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 003 | 4 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | GP R
0SNPQ | 5008153 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 0 | 0 | 4 | U2C_REQ | BACKINV | 000 |
0XQ_DOB | 5008694 | 11000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 001 | 2 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | 00 | GOBU_S Re
0SNPQ | 5009220 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | -- | -- | SNPQ2L2_REQ | -- | 000 | EXT_S
0BBL_L2 | 5009483 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 9 | -- | BBL REQ | L2_UOP_TI | SNP | 0 | 00001100 |
0SNPQ | 5009746 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | -- | -- | SNPQ2XQ_REQ | -- | 000 | EXT_S
0SNPQ | 5009746 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | -- | -- | SNPQ2L2Q_REQ | -- | 000 | EXT_S
0SNPQ | 5010015 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | 0 | 0 | SNPQ2MEC_REQ | -- | 000 | EXT_S
0SNPQ | 5010015 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | 0 | 1 | SNPQ2MEC_REQ | -- | 000 | EXT_S
0SNPQ | 5010015 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | 0 | 2 | SNPQ2MEC_REQ | -- | 000 | EXT_S
0SNPQ | 5010015 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | 0 | 3 | SNPQ2MEC_REQ | -- | 000 | EXT_S
0MEC_BUS | 5010015 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 17 | 3 | -- | -- | BUS2MEC_SNP_REQ | PR2I | 000
0MEC_BUS | 5010015 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 18 | 2 | -- | -- | BUS2MEC_SNP_REQ | PR2I | 000
0MEC_BUS | 5010015 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 19 | 1 | -- | -- | BUS2MEC_SNP_REQ | PR2I | 000
0MEC_BUS | 5010015 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | -- | -- | BUS2MEC_SNP_REQ | PR2I | 000
0SNPQ | 5010541 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | -- | -- | XQ2SNPQ_RSP | -- | 000 | EXT_S
0SNPQ | 5010541 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | -- | -- | L2Q2SNPQ_RSP | -- | 000 | EXT_S
0BBL_L2 | 5010804 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 9 | 0 | L2 RSP | L2_UOP_TI | SNP | 0 | 00001100 |
0SNPQ | 5011067 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | 0 | 0 | MEC2SNPQ_RSP | -- | 000 | EXT_S
0SNPQ | 5011067 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | 0 | 1 | MEC2SNPQ_RSP | -- | 000 | EXT_S
0SNPQ | 5011067 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | 0 | 2 | MEC2SNPQ_RSP | -- | 000 | EXT_S
0SNPQ | 5011067 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | 0 | 3 | MEC2SNPQ_RSP | -- | 000 | EXT_S
0MEC_BUS | 5011067 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 17 | 3 | -- | -- | MEC2BUS_SNP_RSP | PR2I | 000
0MEC_BUS | 5011067 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 18 | 2 | -- | -- | MEC2BUS_SNP_RSP | PR2I | 000
0MEC_BUS | 5011067 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 19 | 1 | -- | -- | MEC2BUS_SNP_RSP | PR2I | 000
0MEC_BUS | 5011067 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | -- | -- | MEC2BUS_SNP_RSP | PR2I | 000
0SNPQ | 5011330 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | -- | -- | -- | L22SNPQ_RSP | -- | 000 | EXT_S
0XQ_DOB | 5011593 | 11000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 002 | 3 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | 00 | GOBU_S Re
0MEC_BUS | 5011856 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | MEC2BUS_SNP_DATA | PR2I | 000
0XQ_DOB | 5012119 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 000 | 5 | DCU_EVICTION | 0 | 36 | SNPQwan
0XQ_DOB | 5013960 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 000 | 5 | CSH_IDI_C2U_REQ_OPCODE_WbMtoI | 0 | 36 | FDB Dat

## Slide 16: grep -h ld_aloc_1000004 *.trk | sort -n --field-separator='|' --key=2 | cut -c-169
0XQ_DOB | 5013960 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 000 | 5 | CSH_IDI_C2U_REQ_OPCODE_WbMtoI | 0 | 36 | FDB Dat
0XQ_DOB | 5013960 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 000 | 5 | CSH_IDI_C2U_REQ_OPCODE_WbMtoI | 0 | 36 | FDB Dat
0XQ_DOB | 5013960 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 000 | 5 | CSH_IDI_C2U_REQ_OPCODE_WbMtoI | 0 | 36 | FDB Dat
0XQ_DOB | 5013960 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 000 | 5 | CSH_IDI_C2U_REQ_OPCODE_WbMtoI | 0 | 36 | FDB Dat
0MEC_BUS | 5014223 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | MEC2BUS_DATA | PR2I | 000
0MEC_BUS | 5014486 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | MEC2BUS_DATA | PR2I | 000
0MEC_BUS | 5014749 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | MEC2BUS_DATA | PR2I | 000
0MEC_BUS | 5015012 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | MEC2BUS_DATA | PR2I | 000
0MEC_BUS | 5015012 | 000011000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 20 | 0 | 54 | -- | BUS2MEC_MEM_COMPL | PR2I | 000
0XQ_DOB | 5015275 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 000 | 5 | DCU_EVICTION | -- | -- | New c2udp
0XQ_DOB | 5015801 | 11000000 | ld_aloc_1000004_rch_snp_0000001_ld_aloc_1000004 | 000 | 5 | DCU_EVICTION | 0 | 36 | SNPQd
0XQ_DOB | 5015801 | 11000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 001 | 2 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | RLB_Data
0XQ_DOB | 5016064 | 110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 003 | 4 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | 00 | GOBU_S Re
0XQ_DOB | 5018168 | 11000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 001 | 2 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | RLB_Data
0XQ_DOB | 5018694 | 0 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 000 | 0 | L2_EVICTION | 1 | 00 |
0XQ_DOB | 5019220 | 0 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 000 | 0 | L2_EVICTION | 1 | 00 | BBLdeal
0XQ_DOB | 5019220 | 0 | ld_aloc_1000004_l2_evic_1000000_ld_aloc_1000004 | 000 | 0 | L2_EVICTION | -- | -- | New c2udp
0BBL_L2 | 5020015 | 000011000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 10 | -- | BBL REQ | L2_UOP_TWW | -- | 0 | 00001100 |
0XQ_DOB | 5020278 | 11000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 001 | 2 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | BBLdea
0BBL_L2 | 5020804 | -- | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 10 | -- | BBL DATA | L2_UOP_TWW | ACTUAL DATA | -- | -- |
0BBL_L2 | 5020804 | -- | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 10 | -- | BBL DATA | L2_UOP_TWW | ACTUAL DATA | -- | -- |
0BBL_L2 | 5020804 | 000011000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 10 | -- | BBL DATA | L2_UOP_TWW | -- | 0 | 00001100 |
0BBL_L2 | 5020804 | 000011000040 | ld_aloc_1000004_l2_pref_1000000_l2_pref_1000000 | 10 | -- | BBL DATA | L2_UOP_TWW | -- | 0 | 00001100 |
0XQ_DOB | 5021067 | 11000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 002 | 3 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | RLB_Data
0XQ_DOB | 5023171 | 11000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 002 | 3 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | RLB_Data
0BBL_L2 | 5025012 | 000011000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 11 | -- | BBL REQ | L2_UOP_TWW | -- | 0 | 00001100 |
0XQ_DOB | 5025275 | 11000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 002 | 3 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | BBLdea
0BBL_L2 | 5025801 | -- | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 11 | -- | BBL DATA | L2_UOP_TWW | ACTUAL DATA | -- | -- |
0BBL_L2 | 5025801 | -- | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 11 | -- | BBL DATA | L2_UOP_TWW | ACTUAL DATA | -- | -- |
0BBL_L2 | 5025801 | 000011000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 11 | -- | BBL DATA | L2_UOP_TWW | -- | 0 | 00001100 |
0BBL_L2 | 5025801 | 000011000080 | ld_aloc_1000004_l2_pref_1000001_l2_pref_1000001 | 11 | -- | BBL DATA | L2_UOP_TWW | -- | 0 | 00001100 |
0XQ_DOB | 5026064 | 110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 003 | 4 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | RLB_Data
0XQ_DOB | 5028431 | 110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 003 | 4 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | RLB_Data
0BBL_L2 | 5030278 | 0000110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 12 | -- | BBL REQ | L2_UOP_TWW | -- | 0 | 00001100 |
0XQ_DOB | 5030541 | 110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 003 | 4 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt_Pref | 1 | c0 | BBLdea
0BBL_L2 | 5031067 | -- | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 12 | -- | BBL DATA | L2_UOP_TWW | ACTUAL DATA | -- | -- |
0BBL_L2 | 5031067 | -- | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 12 | -- | BBL DATA | L2_UOP_TWW | ACTUAL DATA | -- | -- |

## Slide 17: grep -h ld_aloc_1000004 *.trk | sort -n --field-separator='|' --key=2 | cut -c-169
0BBL_L2 | 5031067 | -- | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 12 | -- | BBL DATA | L2_UOP_TWW | ACTUAL DATA | -- | -- |
0BBL_L2 | 5031067 | -- | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 12 | -- | BBL DATA | L2_UOP_TWW | ACTUAL DATA | -- | -- |
0BBL_L2 | 5031067 | 0000110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 12 | -- | BBL DATA | L2_UOP_TWW | -- | 0 | 00001100 |
0BBL_L2 | 5031067 | 0000110000c0 | ld_aloc_1000004_l2_pref_1000002_l2_pref_1000002 | 12 | -- | BBL DATA | L2_UOP_TWW | -- | 0 | 00001100 |
0XQ_DOB | 5033960 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 000 | 1 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt | 1 | 00 | GOBU_E Re
0MEC_BUS | 5034223 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | -- | BUS2MEC_MEM_GO | DCU_READ | 000
0XQ_DOB | 5040541 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 000 | 1 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt | 1 | 3e | RLB_Data
0MEC_BUS | 5041067 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | -- | BUS2MEC_DATA | DCU_READ | 000
0MEC_BUS | 5041067 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | -- | BUS2MEC_DATA | DCU_READ | 000
0XQ_DOB | 5043171 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 000 | 1 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt | 1 | 3e | RLB_Data
0MEC_BUS | 5043697 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | -- | BUS2MEC_DATA | DCU_READ | 000
0MEC_BUS | 5044223 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 8 | 1 | 62 | -- | BUS2MEC_MEM_COMPL | DCU_READ | 000
0BBL_L2 | 5045012 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 13 | -- | BBL REQ | L2_UOP_TWW | -- | 0 | 00001100 |
0XQ_DOB | 5045275 | 11000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 000 | 1 | CSH_IDI_C2U_REQ_OPCODE_DRd_Opt | 1 | 3e | BBLdea
0BBL_L2 | 5045801 | -- | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 13 | -- | BBL DATA | L2_UOP_TWW | ACTUAL DATA | -- | -- |
0BBL_L2 | 5045801 | -- | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 13 | -- | BBL DATA | L2_UOP_TWW | ACTUAL DATA | -- | -- |
0BBL_L2 | 5045801 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 13 | -- | BBL DATA | L2_UOP_TWW | -- | 0 | 00001100 |
0BBL_L2 | 5045801 | 000011000000 | _____NA_0000000_ld_aloc_1000004_ld_aloc_1000004 | 13 | -- | BBL DATA | L2_UOP_TWW | -- | 0 | 00001100 |

## Slide 18: Validation Recommendations
Standardize the formatting of the Time and Address
Further URI validation use the URI as key to search and make sure it matches to DCUID,…
Use for further checking
    promotions
    For homeless requests
    external complete (IDI)
    LLC Pref go (IDI)
    In case of MCA when multiple errors are colliding in the MCA logic
      Need RTL support

## Slide 19: RTL Recommendations
Print the URI when flagging an SVA